Dynaban :
An alternative firmware for
Dynamixel servos
Rhoban team
http://www.rhoban.com/

---
Dynamixel
- Robotis Dynamixel servos : standard for low-cost robotics
- Good mechanics and motor (usually Maxon)
- Handy serial daisy chainable half-duplex Dynamixel protocol
- Electronics features : accurate magnetic encoder (for MX serie), current sensing, thermistor (temperature), integrated H-bridge

---
The firmware
- These servos feature a programmable µController
- The original firmware is NOT open-source
  → We decided to write a custom alternative firmware for those servos

---
Why ?
- Imagine having control on what happens inside the servo
- Robocupians are mainly software developers (aren't they?)...
- … and like open-source !

---
Diving into MX64
- ~200 U.S.$
- Features Maxon motor
- 200:1 Gearbox

---
Diving into MX64
- µController : STM32F103
  - 32bit @72Mhz, 120k flash 20k ram
  - Widespread ARM Cortex-M3

---
Diving into MX64
- Magnetic encoder
  - AS5045 chip
  - Using a hall-effect sensor array
  - Know the orientation of a magnet
  - 12 bits / 20khz

---
Diving into MX64
- H-bridge (using drivers & mosfets)
- Half-duplex driver for serial communication
- Current sensing
  - 0,005 ohm sensing resistor
  - MAX9918 amplifier
- Thermistor
- Voltage divider (3/23)
- Two linear regulators : 3.3V & 5V ← Heat

---
How ?
- Servos comes with integrated serial bootloader
- BTW, it's programmable via RoboPlus
- We first wrote our own script to flash servos (sending custom binaries)

---
Writing firmware
- Previous experiences on STM32 using Maple Mini
- We based our project on libmaple, a STM32 library
  - Arduino-like functions
  - Mainly C, some C++

---
Danger !
- First test : BOOM !
  - We broke a servo trying to drive its motor, the mosfets exploded !
- Be careful !
  - A bad firmware can break the servo
  - Custom firmware voids servo warranty
  - Robotis doesn't sell electronics separately

---
Writing firmware
- What our firmware currently DOES :
  - Drive the LED
  - Sample the encoder (position) and the current (torque)
  - Communicate through serial with Dynamixel 1.0 protocol (not all features are implemented… yet)
  - Drive the motor, with safe abstraction layer
  - Servoing the position using PID controller
  - Proof of concepts for torque servoing

---
Writing firmware
- What we plan to do (soon) :
  - Finish the implementation of the protocol
  - Fancy control loops (torque control)
  - Clean the code (as much as possible)
  - Open-source the code !

---
Writing firmware
- Possibilities :
  - Reducing the power consumption ? (Underclocking?)
  - Adding features
    - Optimizing protocol ?
    - Sending pre-timed trajectories ?
  - Creating open-source electronics ?
  - Insist on Robotis to release open-source servos :-)

---
Demonstration

---
Questions

---
Thanks for listening